# Introduction

The main goal of this guide is to use the FlashSim simulator as described here:

http://csl.cse.psu.edu/?q=node/322

This guide assumes that all steps to setup DiskSim 3.0 were done according to the following guide:

http://www.pdl.cmu.edu/DiskSim/Compiling_DiskSim3.0_v1.0.pdf

Once you have DiskSim 3.0 successfully running per the above guide, use the instructions in this doc to get FlashSim compiled and running.

# Helpful Links

# DiskSim Users Email list

https://sos.ece.cmu.edu/mailman/listinfo/disksim-users

# Ajay’s Guide for DiskSim

http://www.cs.rice.edu/~gulati/

# Original DiskSim Website

http://www.pdl.cmu.edu/DiskSim/

Using FlashSim with DiskSim 3.0

http://csl.cse.psu.edu/?q=node/322

Compiling DiskSim 3.0

http://www.pdl.cmu.edu/DiskSim/Compiling_DiskSim3.0_v1.0.pdf

# Environment

See the Compiling DiskSim 3.0 guide.

# Software

See the Compiling DiskSim 3.0 guide.

# Procedures

- Install indent:
sudo apt-get install indent

- Verify that the indent is installed (I installed version 2.2.10-3):
indent --version
#Output on screen shows: GNU indent 2.2.10

- Download the src.release.20101205.tar.gz.

Note: The original files from src.release.jontjioe.tar.gz can be downloaded here:

http://csl.cse.psu.edu/?q=node/322. The reason why I re-packaged is because with this new package (src.release.20101205.tar.gz), the patch that was made by Khalifa Rouis has already been run. Additionally, there were about 15-20 lines that had fprintf statements that were spanned across multiple lines. I joined the lines for these statements so that FlashSim was able to compile successfully. By repackaging it, you do not have to modify these files again.

Note: In all steps below, replace “/home/jontjioe/disksim/disksim-3.0” with the path to your disksim installation.

- Save the current src directory in DiskSim 3.0.
cd /home/jontjioe/disksim/disksim-3.0
mv src src.orig

- Extract the FlashSim src directory (contains DiskSim 3.0 and FlashSim source files) to your disksim directory.
cp src.release.20101205.tar.gz /tmp
cd /tmp
gunzip src.release.20101205.tar.gz
tar –xvf src.release.20101205.tar
mv src.release.20101205.tar /home/jontjioe/disksim/disksim-3.0/src

Note: You should now have the new src directory in your disksim-3.0 directory.

- Update the .paths and .paths.in files inside the src directory to have your disksim directory.

export DISKMODEL_PREFIX=/home/jontjioe/disksim/disksim-3.0/diskmodel
export LIBPARAM_PREFIX=/home/jontjioe/disksim/disksim-3.0/libparam
export LIBDDBG_PREFIX=/home/jontjioe/disksim/disksim-3.0/libddbg

cp .paths.in .paths

- Compile the src directory.
make

- Download the test.release.tar.gz from here:
http://csl.cse.psu.edu/?q=node/322

- Extract the FlashSim test directory to your disksim directory.
cp test.release.tar.gz /tmp
cd /tmp
gunzip test.release.tar.gz
tar –xvf test.release.tar
mv test.release /home/jontjioe/disksim/disksim-3.0/test

Note: You should now have the new test directory in your disksim-3.0 directory.

- Verify that FlashSim is running properly.
cd /home/jontjioe/disksim/disksim-3.0/test
./runtest

You should see the following output on the screen if it is working:

Running Pagemap FTL...
IOdriver Response time average: 	0.429880
IOdriver Response time std.dev.:	0.802131
Running DFTL...
IOdriver Response time average: 	0.609340
IOdriver Response time std.dev.:	1.513767
Running FAST...
IOdriver Response time average: 	3.189379
IOdriver Response time std.dev.:	23.326385